Problem Set #2

- Three small particles are connected by rigid rods of negligible mass lying along the y-axis.  A 4.00-kg mass is at y = 3.00 m, a 2.00-kg mass is at y = -2.00 m, and a 3.00-kg mass is at y=-4.00 m.  If the system rotates about the x-axis with an angular speed of 2.00 rad/s, find

  - the rotational inertia about the x-axis

  - the total rotational kinetic energy

  - the linear speed of each particle

  - the total kinetic energy evaluated from ( ½ mv2

- The center of mass of a pitched baseball (3.80 cm radius) moves at 38.0 m/s.  The ball spins about an axis through its center of mass with an angular speed of 125 rad/s.  Calculate the ratio of the rotational energy to the translational kinetic energy.  Treat the ball as a uniform sphere.

- Use the parallel axis theorem to find the moments of inertia of

  - a solid cylinder about an axis parallel ot the center-of-mass axis and passing through the edge of the cylinder and

  - a solid sphere about an axis tangent to its surface.

- A 1.3-kg bicycle wheel of radius 70.0 cm rotates at 19 rad/s.  Note – the wheel can be treated as a hoop.

  - What is its rotational kinetic energy?

  - What is the linear speed of the wheel?

  - What is the radial acceleration of the wheel?

- Two 5.00-kg masses are attached to the ends of a 12.0-kg thin rod that is 10.0 m long.  The system is rotated about a perpendicular axis 2.0 m from its left end and 8.0 m from its right end.

  - What is the rotational inertia of the system?

  - If the axis can be shifted left or right any amount, what is the minimum rotational inertia for this system?