Interpretation Questions

- Eduardo acquired the following data:

| Weight Added | Spring Position |
| --- | --- |
| 0 | 30 cm |
| 0.6 N | 52 cm |
| 1.0 N | 71 cm |
| 1.2 N | 80 cm |
| 2.4 N | 124 cm |
| 3.0 N | 152 cm |

- What is the spring constant of the spring?

- The spring is now stretched 80 cm (from its rest position). How much energy is stored in the spring?

- A 500-g mass is attached to the spring when it is in the position described above and is released from rest.  What is the frequency of its oscillation?

- What is the maximum speed attained by the 500-g mass?

- Two springs of k-value 40 N/m hang from a ring stand.  A 1.6-kg mass is attached to both springs. How far do the two springs stretch when the mass hangs in equilibrium?

- In the previous question, how far would the spring stretch if the two springs were attached end-to-end on the ring stand?

- The table below gives the distance of a weight on the end of a spring as it bobs up and down.  The distance is measured from the top of a table.

| TIME (s) | DIST (cm) |
| --- | --- |
| 0.5 | 11 |
| 0.6 | 17 |
| 0.7 | 20 |
| 0.8 | 21 |
| 0.9 | 20 |
| 1.0 | 17 |
| 1.1 | 11 |
| 1.2 | 5 |
| 1.3 | 2 |
| 1.4 | 1 |
| 1.5 | 2 |
| 1.6 | 5 |
| 1.7 | 11 |
| 1.8 | 17 |
| 1.9 | 20 |

- What is the period of the above motion?

- What is the frequency of the above motion?

- What is the amplitude of the above motion?

- A 0.5 kg mass is attached to a spring and oscillates in simple harmonic motion with an amplitude of 0.24 m. The maximum speed of the vibrating mass is 0.6 m/s.

- Calculate the value of the spring constant.

- What is the maximum acceleration of the vibrating mass?